## Slide 1: Design of RF & Microwave Systems
Xiaoguang “Leo” Liu
Assistant Professor
School of Electrical and Computer Engineering
Tel: 530-289-6367
lxgliu@ucdavis.edu
http://ucdart.net
EEC 134 A&B
Lecture 8: Building Blocks of RF Systems
– (De)Modulation and (De)Modulators

## Slide 2: Modulation
Encode low frequency information onto a high frequency carrier
  Both analog and digital
  Need to consider signal quality (analog) or error rate (digital) in the presence of noise, efficient utilization of frequency bandwidth, efficient utilization of power
There are two independent variables in a cosine (or sine) carrier
  Amplitude
  Phase (Frequency is the derivative of phase!)
Amplitude
Frequency
Phase
http://www.studyvilla.com/modultn.aspx
Analog Modulations

## Slide 3: Amplitude Modulation
Simple to realize: need one mixer
Signal quality depends on amplitude noise and circuit linearity (because amplitude carries the information)
B. Razavi, UCAL EE215C Lecture notes
Notes: Change to own graph

## Slide 4: Phase and Frequency Modulation
Mostly insensitive to non-linearity; can use a non-linear power amplifier (therefore system efficiency is higher)
  Some phase and frequency modulation does incur amplitude variation
Typically occupies more bandwidth
Since frequency is the derivative of phase, frequency modulation can be considered a special case of phase modulation. It is for this reason that frequency and phase modulation are sometimes called angle modulation altogether
B. Razavi, UCAL EE215C Lecture notes
Notes: Change to own graph

## Slide 5: Digital Modulation
Modulation of digital signals is also known as Shift Keying
  Amplitude Shift Keying (ASK)
  Frequency Shift Keying (FSK)
  Phase Shift Keying (PSK)
  More advanced modulation schemes: QPSK, DQPSK, MFSK, MSK/GMSK, QAM, CPM, etc
ASK
FSK
PSK
Read more: http://en.wikipedia.org/wiki/Digital_modulation#Digital_modulation_methods

## Slide 6: Quadrature Amplitude Modulation
Combines both amplitude and phase (angle) modulation
More efficient use of spectrum
Transmits a complex signal -- a very general representation of modulation
  A carrier signal has two components that can carry information: amplitude and phase
  Therefore a sinusoidal signal is really “two-dimensional”. It can be represented in either 1) amplitude and phase, 2) real and imaginary parts
In-phase
Quadrature
Am
ϕm
I
Q

## Slide 7: Constellation Diagram
Representation of the modulated signal on a complex plane according to its amplitude and phase modulation (or in-phase and quadrature modulation)
8-PSK
16-QAM

## Slide 8: Quadrature Modulation
I/Q
Generator
Base-band
Signal
Σ
I(t)
Q(t)

## Slide 9: Quadrature Modulation
I/Q
Generator
Base-band
Signal
Σ
-90°
I(t)
Q(t)

## Slide 10: How do We Generate the Quadrature Signals?
Quadrature hybrid!!
I/Q
Generator
Base-band
Signal
Σ
90° Hybrid
I(t)
Q(t)

## Slide 11: Quadrature Demodulation

## Slide 12: Quadrature Demodulation
I/Q
Generator
Base-band
Signal
Σ
I(t)
Q(t)
-90°
I(t)
Q(t)

## Slide 13: Quadrature Demodulation in a Doppler Radar Receiver
Simple mixer
  Since , positive and negative speed can not be differentiated, i.e. you can only measure the speed but can’t tell if the object is moving towards you or away from you

## Slide 14: Quadrature Demodulation in a Doppler Radar Receiver
Quadrature demodulator
  The quadrature output is different for positive and negative Doppler frequency shift
-90°
-90°

## Slide 15: IQ Demodulation Imperfections
In a practical demodulation circuit, it may be difficult to have a precisely aligned receiver LO frequency and phase
What if
  LO has a slightly different frequency?
  LO has a slightly different phase?
  The quadrature LOs are not exactly in quadrature?
  The quadrature LOs have slightly different amplitude?

## Slide 16: IQ Demodulation Imperfections
Example: slight demodulator LO frequency offset
  Received in-phase signal has a component from the quadrature signal
  Lead to error in the demodulation if the frequency offset is large enough
Similarly, other imperfections can lead to signal demodulation errors

## Slide 17: Signal Distortion viewed on the Constellation Diagram

## Slide 18: Error Vector Magnitude (EVM)
In digital transmission, several factors can cause perturbation to the signal
  Noise in the propagation channel
  Noise and non-linearity in the transmit and receive circuits
  Imperfect modulation and demodulation circuit
    Phase noise of the LO signals in Tx and Rx
    LO phase and amplitude mismatch
Error vector magnitude (EVM) is used to quantify the amount of distortion to the modulated signal
  Defined based on the constellation diagram
is the I component of the j-th symbol received, is the Q component of the j-th symbol received, is the ideal I component of the j-th symbol received, is the ideal Q component of the j-th symbol received.
http://www.ni.com/white-paper/3652/en/
http://www.hometoys.com/emagazine.php?url=/htinews/feb05/articles/chipcon/zigbee.htm

## Slide 19: IQ (Quadrature) Modulator Example
Texas Instruments TRF370417 50 MHz – 6 GHz Quadrature Modulator IC

## Slide 20: IQ (Quadrature) Modulator Example
Texas Instruments TRF371135 1.7– 6 GHz Quadrature Demodulator IC (direct down-conversion receiver)
RF in
LO
Baseband
In-phase
Baseband
Quadrature
Quadrature
Generator

## Slide 21: Single Side Band Modulation and Image Reject Mixers
The concept of quadrature modulation also finds application in two other areas
  Single side band modulation
  Image reject mixers

## Slide 22: Single Side Band Modulation
Consider a simple AM modulator with a mixer
  There are two sidebands with identical information: not very efficient use of spectrum
  Ideally you just want to transmit one sideband because it has all the information
  You can filter the other sideband but sometimes this would require a very sharp (and therefore lossy) filter
B. Razavi, UCAL EE215C Lecture notes

## Slide 23: Single Side Band Modulation
Base-band Signal
Σ
-90°
90°

## Slide 24: Single Side Band Modulation
If we take 90° phase shift of the LO, i.e. use instead of , we can get the difference frequency
Base-band Signal
Σ
90°
90°

## Slide 25: Single Side Band Modulation
Visualization in the frequency domain
  Multiplication in time domain is convolution in frequency domain
Base-band Signal
Σ
90°
90°
X
X
+

## Slide 26: Image Reject Mixer
The quadrature signals can also help to eliminate the image problem
The Hartley image reject mixer
  Introduced in 1928
  Quadrature LO
  90° phase shift of one of the IF signals
http://www.microwavejournal.com/articles/3226-on-the-direct-conversion-receiver-a-tutorial
An alternative Hartley image reject mixer, allowing both the signal and image to be captured

## Slide 27: Image Reject Mixer
The Weaver image reject mixer
  Using two quadrature LOs
  Does not need a separate 90° phase shifter
http://www.microwavejournal.com/articles/3226-on-the-direct-conversion-receiver-a-tutorial

## Slide 28: Image Reject Mixer
The performance of both the Hartley and the Weaver image reject mixers reply on the accuracy of the phase quadrature and amplitude balance
http://www.microwaves101.com/encyclopedias/image-rejection-mixers

## Slide 29: Image Reject Mixer Example
Mini-Circuits JCIR-25+
The quadrature output of the 90° hybrid is terminated to 50 Ω