## Slide 1: Design of RF & Microwave Systems
Xiaoguang “Leo” Liu
Assistant Professor
School of Electrical and Computer Engineering
Tel: 530-289-6367
lxgliu@ucdavis.edu
http://ucdart.net
EEC 134 A&B
Lecture 9: System Concepts
– Receiver Architecture

## Slide 2: RF System Design Topics
From this lecture on, we will discuss several topics related to RF/microwave system designs
  Transmitter and receiver architectures
  Design and estimation of system gain, noise, and non-linearity
  Link budget calculation

## Slide 3: General Considerations of RF Systems Design
Transmitter
  Output power
  Spurious emission
  Linearity
  Efficiency
  Complexity
Receiver
  Sensitivity (noise)
  Gain
  Linearity
  Selectivity (Immunity to Interference)
  Complexity
Transmitter
Receiver
Notes: What is needed in the receiver front-end?
• Amplification to compensate for transmission losses
• Selectivity to separate the desired signal from others
• Tunability to select the desired signal
• Conversion to digital domain

## Slide 4: Interference

## Slide 5: Interference
Interference: unwanted out-of-band or in-band signals
In practical RF system designs, interference may become the limiting factor in system performance. They must be taken into account in the design phase
LightSquared is a company that tries to develop a wholesale 4G wireless network integrated with satellite coverage across the United States.
In 2004, LightSquared acquired authorization from FCC to use the 1525 – 1559 MHz spectrum for its broadband 4G network. The Global Positioning System (GPS) uses the 1559 – 1610 MHz, which is really close
After LightSquared started deploying some of its base-stations, people noticed strong interference to some existing GPS receivers. The GPS community has since opposed the deployment of LightSquared networks. Interestingly, only those GPS receivers without a front-end filter were affected.
In 2012, FCC moved to bar LightSquared’s network because interference issues
In May 2012, LightSquared filed for bankruptcy. LightSquared has since lost $ 1.6 Billion and the figure is still rising…
Read more: http://en.wikipedia.org/wiki/LightSquared

## Slide 6: Front-end Filtering May NOT be Enough
Sometimes interferers are too close to the desired signal that the front-end filter cannot be completely eliminate the interferer.
  The required filter may be too narrow-band that its loss can not be tolerated by the receiver
The front-end filter usually selects a band of frequency around the desired signal, allowing some interferers to pass through
  Any receiver components must be linear enough to accommodate the interferer alongside the desired signal
  Recall the non-linearity discussion in the RF Amplifiers lectures; strong interferers may desensitize or saturate the first receiver amplifier
B. Razavi, UCAL EE215C Lecture notes

## Slide 7: Transmitter Spurious Emission
The non-linearity of the transmitter power amplifier may cause out-of-band emission and must be well controlled
  The sideband of a modulated signal rise significantly as the power amplifier enters compression and saturation region
  The power amplifier must be sufficiently linearized
  Or a strong filter will need to be used before the signal is transmitted to the antenna
http://mwrf.com/test-and-measurement/wireless-laboratory-aids-students-and-research
A very low-loss output filter for base stations
B. Razavi, UCAL EE215C Lecture notes

## Slide 8: Receiver Architectures
Superheterodyne vs. Direct Conversion

## Slide 9: Band Selection and Channel Selection
Example: Global System for Mobile Communications (GSM) – 2G cellular standard
  A GSM system has 124 pairs of simplex (meaning only transmit or only receive) channels, each of 200-kHz wide.
  Selecting a channel (0.2 MHz) at the RF frequency (~900 MHz) is very difficult, if not impossible
http://www.thatstechnology.com/what-is-gsm-global-system-for-mobile-communications/
B. Razavi, UCAL EE215C Lecture notes

## Slide 10: Superheterodyne (SuperHet) Receiver
Moves RF frequency to an intermediate frequency (IF) before further processing
  Easier to amplify the signals at lower frequency
  Can distribute system gain at different frequencies to prevent oscillation
  Selecting the channel is easier at lower frequency
  A common architecture is to sweep the LO frequency to accommodate a band of RF signals
  Note that it is possible to use an LO frequency higher than the RF

## Slide 11: SuperHet
RF filter is only capable for band selection
  Generally fixed in frequency (tunable RF filters with sufficient high Q is extremely, if not impossible, to make)
Channel selection happens at the IF frequency, where very narrowband filter are possible
  Consider the following: 1 MHz bandwidth is 0.1% at 1 GHz but 10% at 10 MHz
  Components have much higher Q at lower frequencies
  Generally a low IF makes it easier to do channel selection; but a low IF also make the image very close to the actual signal; making it hard to filter

## Slide 12: SuperHet – Image Problem
Image reject mixer will help to a certain extent
  Common image reject mixers have image rejection ratio of 25-40 dB; may not be enough for a high power (> 60 dBc) interferer at the image frequency
  Front-end filter (before the LNA) or an image reject filter (after the LNA, could be low pass or bandpass) may be needed
B. Razavi, UCAL EE215C Lecture notes

## Slide 13: SuperHet – Dual Downconversion
It is possible to use more than one IF frequency
  Better selectivity
  Better distribution of gain
  Usually result in high sensitivity and dynamic range
  More complex
  Mixer spurs; recall that each mixing operation creates frequency components
  Frequency plan needs to be carefully considered
  Requires more components, thus expensive
B. Razavi, UCAL EE215C Lecture notes

## Slide 14: Up-Conversion SuperHet
It is also possible to use an IF higher than the RF
  Seems counterintuitive: isn’t circuit design easier at low frequencies?
  Image problem is greatly alleviated!!
  Usually only the first stage is up-conversion
Low IF
High IF
Image Reject Filter
Image Reject Filter

## Slide 15: Example: A Spectrum Analyzer
Many spectrum analyzers use a high IF for their first stage
RF:
0 – 1.75 GHz
First LO:
2.1 – 3.85 GHz
First IF:
2.1 GHz
Second IF:
70 MHz
Third IF:
10 MHz
Second LO:
2.03 GHz
Third LO:
60 MHz
http://lea.hamradio.si/~s53mv/spectana/vco.html

## Slide 16: Direct Conversion Receiver
What if we set the IF to be 0? i.e. directly convert RF to baseband?
  Entirely possible! We call such a receiver zero-IF or direct conversion receiver; another name for it is homodyne (which in fact has a slightly different meaning)
There is no image frequency! Image reject filters are not needed anymore
  System complexity reduces significantly; very amenable to IC design
  LNA does not have to drive 50 Ω; can now use a current mode LNA to improve linearity
  Tuning the LO tunes the RF; easier to design a tunable RF receiver
Channel selection is performed by a fixed low pass filter
http://www.eetimes.com/document.asp?doc_id=1276400

## Slide 17: Direct Conversion Receiver – Problems
No free lunch! Direct conversion receivers have their own problems
  LO Leakage
  DC Offset
  I/Q Mismatch
  Even-order distortion
  Flicker Noise
Direct conversion receiver was invented in the 1930s, but the above technical issues prevented it from being used until recently
The development in large scale integrated circuits and a need to have very tunable and re-programmable RF system (software defined radio) have revived it

## Slide 18: LO Leakage
Since LO and RF are of the same frequency, the LO signal can pass through all the front-end filters and the antenna
  Leakage of the LO may radiate from the receiving antenna, causing interference to other users. You are transmitting on a receive frequency!
  Leakage can happen through substrate coupling, an insufficient LO-RF isolation in the de-modulator/mixer, and an insufficient reverse isolation in the LNA
http://mwrf.com/components/quad-demodulators-arm-direct-conversion-receivers

## Slide 19: DC Offset
When the leakage LO comes back to the de-modulator/mixer, it will mix with the actual LO to create a dc component at the baseband
  LO leakage may reflect at the component boundaries where there is a mismatch
  The radiated LO leakage may reflect off a nearby object to come back through the antenna
http://mwrf.com/components/quad-demodulators-arm-direct-conversion-receivers

## Slide 20: DC Offset
Since the offset occurs at dc, we can use a dc-blocking capacitor to eliminate it
  The capacitor would have to be fairly large; may occupy a large chip area if the circuit is to be implemented with IC technology
  Charging of the capacitor also takes time, making it hard to accommodate fast data rates
  Dc-blocking won’t work for signals whose baseband spectrum has a dc component itself
B. Razavi, UCAL EE215C Lecture notes

## Slide 21: Even Order Distortion
We learned about non-linearity in the RF Amplifiers lecture and know that third-order non-linearity lead to inter-modulations products that are very close to desired signal
In a direction conversion receiver, there is one more non-linear distortion mechanism: even-order non-linearity
A
Consider the second order term in the amplifier non-linear input-output relationship
With two interferers close to the desired signal frequency
Beat frequency is close to baseband!
B. Razavi, UCAL EE215C Lecture notes

## Slide 22: Even Order Distortion
Beat frequency due to the second-order non-linearity term can pass through the receiver chain if the RF-IF leakage is not well controlled
Because the beat frequency is close to dc, it may corrupt the desired signal
B. Razavi, UCAL EE215C Lecture notes

## Slide 23: Second-Order Intercept Point
Similar to the concept of IP3, we define a second-order intercept point (IP2) for the receiver
  In general, all even-order non-linearities create the low-frequency beat signals; the second-order term is usually the strongest of them
  IP2 defined as the point when the second-order inter-modulation products have the same power as the fundamental term
B. Razavi, UCAL EE215C Lecture notes

## Slide 24: Even Order Distortion
Even-order distortion will also cause a low frequency output if the interferer has amplitude variations
  The second-order term essentially works as a square-law detector
  One interferer is enough to cause trouble to your baseband signal
A
The envelop signal will pass through the baseband LPF
B. Razavi, UCAL EE215C Lecture notes

## Slide 25: Flicker Noise
Flicker noise is a type of frequency dependent noise (compare with thermal noise, which is frequency independent for practical applications)
  Flicker noise shows up as a low-frequency variation in the current or voltage in an electronic device
  Flicker noise in an electronic device is always associated with a dc current
  Also know as 1/f noise, as the slope of noise power follows a 1/f relationship; or pink noise, as opposed to white noise
  Flicker noise is usually characterized by its corner frequency fc
http://mwrf.com/test-and-measurement/integrated-system-tests-device-flicker-noise
MOSFETs (such as CMOS transistors) have a higher fc (0.1 – 1 MHz) than JFET or bipolar transistors (could be as low as 2 kHz)

## Slide 26: Flicker Noise in a Direction Conversion System
Since RF signal is de-modulated into basedband directly, they suffer from flicker noise in the baseband amplifier
http://mwrf.com/components/quad-demodulators-arm-direct-conversion-receivers

## Slide 27: Superheterodyne vs. Direct Conversion
Superheterodyne
  Superior performance in terms of sensitivity and dynamic range
  Complex system design and frequency planning
  Requires more components, especially high-Q filters that may be difficult to integrate into IC
  Difficult to tune to a wide frequency range
Direct conversion
  Flexibility in RF frequency
  Fewer components, especially filters
  Lower cost
  Suffer from a few issues that need to be carefully taken care of
    DC offset
    IQ imbalance
    LO leakage
    Flicker noise

## Slide 28: Low IF Receiver
Low IF: IF in the range of a few MHz or several hundred kHz
Advantages:
  Great channel selection capability
  Very much like direct conversion receiver, but without the problems of DC offset and flicker noise.
  May require less components
Disadvantages:
  Image frequency is very close to the RF frequency; may need a very high-Q filter; image reject mixer not be sufficient
    This can be alleviated if we know for sure that there will not be interferers at the image frequency
http://www.edom.com.tw/en/index.jsp?lang=en&m=techview&cal=9&id=1383
Analog low-IF FM receiver
Digital low-IF FM receiver
Low-IF receivers are very popular in modern miniature FM receivers
  Interferers are well known; no stronger transmitting signal in vicinity