## Slide 1: Design of RF & Microwave Systems
Xiaoguang “Leo” Liu
Assistant Professor
School of Electrical and Computer Engineering
Tel: 530-289-6367
lxgliu@ucdavis.edu
http://ucdart.net
EEC 134 A&B
Lecture 2: Basics Concepts

## Slide 2: Outline
Review of transmission lines
  Refer to the “Lec2-ReviewTransmissionLines.pptx”, which contains excerpts from 130A course materials
The Radio Spectrum
Units in RF engineering
Scattering parameters

## Slide 3: The Radio Spectrum

## Slide 4: Frequency Spectrum Allocation
Radio spectrum is considered a scarce natural resource and is heavily regulated
  Note that regulation only applies to transmitting
Image from Federal Communications Commission (FCC)
Notes: Add introduction to ITU and FCC

## Slide 5: Frequency Spectrum Allocation
Image from Federal Communications Commission (FCC)

## Slide 6: Frequency Spectrum Allocation
Radio Spectrum is expensive
  “Since July 1994, the FCC has conducted 87 spectrum auctions, which raised over $60 billion for the U.S. Treasury” -- Wikipedia
  “The President has set the goal of freeing up 500 MHz of spectrum …within a decade. Critical to realizing this goal are “voluntary incentive auctions” and more efficient use of government spectrum, estimated to raise $27.8 billion over the next decade.”
  -- The White House, 2011
http://www.whitehouse.gov/the-press-office/2011/02/10/president-obama-details-plan-win-future-through-expanded-wireless-access

## Slide 7: Frequency Spectrum Allocation
Unlicensed ISM Bands
  ISM = Industrial, Scientific and Medical
  Your product still needs to pass FCC certification

## Slide 8: Frequency Spectrum Allocation
Amateur Radio Bands

## Slide 9: Units in RF Systems
decibel (dB)
  Ratio between two quantities (usually power or intensity, i.e. square of field)
  Numerically equals to 10 times the logarithm to base 10
Neper
  Natural log based
  You mostly see this unit when specifying attenuation

## Slide 10: Units in RF Systems – A Simple Example
Amplifier
Gain
Only holds when the input and output impedance are equal!
Pin
Pout

## Slide 11: Units in RF Systems
Quick calculations:
  2 × ≈ +3 dB
  0.5 × ≈ -3 dB
  4 × ≈ 6 dB
  0.25 × ≈ - 6 dB
  10 × ≈ 10 dB
  100 × ≈ 20 dB
Why do we want to use dB?
  Log scale converts multiplication to addition/subtraction
Note:
10log2 =3.010,
not exactly 3 dB

## Slide 12: Units in RF Systems
dBm
  Power relative to 1mW in dB scale
  Examples:
    10 mW = 10 dBm
    0 dBm = 1 mW
    30 dBm = ?
Don’t confuse dBm with dB
  dBm is a unit; it represents power
  dB is a pure number; it represents a ratio

## Slide 13: Example
How much is the input power in W?
How much is the output power in W?
Assume the output is connected to a 50 Ω load, what is the RMS voltage on the load?
Amplifier Gain 17 dB
Input 3 dBm

## Slide 14: Typical Power Levels
dBm level | Power | Notes
80 dBm | 100 kW | Typical transmission power of FM radio station with 50-kilometre (31 mi) range
50 dBm | 100 W | Typical thermal radiation emitted by a human body
33 dBm | 2 W | Maximum output from a mobile phone (Power class 1 mobiles)
30 dBm | 1 W | Typical RF leakage from a microwave
27 dBm | 500 mW | Typical cellular phone transmission powerMaximum output from a mobile phone (Power class 2 mobiles)
3 dBm | 2.0 mW | More precisely (to 8 decimal places) 1.9952623 mW
0 dBm | 1.0 mW = 1,000 µW | Bluetooth standard (Class 3) radio, 1 m range
−80 dBm | 10 pW | Typical range (−70 to −90 dBm) of wireless received signal power over a WiFi network (802.11 variants)
−127.5 dBm | 0.178 fW = 178 aW | Typical received signal power from a GPS satellite
From Wikipedia

## Slide 15: Scattering Parameters
RF/microwave circuits
  Voltage/current may not be easily defined
  Open/short hard to make
  Power is easier to work with
    No position dependence
2-Port networks
  Power is either “transmitted”, “reflected”, or “dissipated”
  Work with a standard system impedance: “matched” or “mis-matched”
Agilent Application Note 95-1, “S-Parameter Techniques”

## Slide 16: Scattering Parameters
S-Parameter: Use power quantities instead of voltage or current
The difference between the incident power (the power that would be delivered to a matched load) and the reflected power represents the power delivered to the circuit.
B. Razavi, “RF Microelectronics”, 2nd Ed. 2011

## Slide 17: S-Parameters
S11 is the ratio of the reflected and incident waves at the input port when the reflection from RL is zero.
Represents the effectiveness of the input matching
S12 is the ratio of the reflected wave at the input port to the incident wave into the output port when the input is matched
Characterizes the reverse isolation
B. Razavi, “RF Microelectronics”, 2nd Ed. 2011

## Slide 18: S-Parameters
S22 is the ratio of reflected and incident waves at the output when the reflection from Rs is zero
Represents the effectiveness of the output matching
S21 is the ratio of the wave incident on the load to that going to the input when the reflection from RL is zero
Represents the gain (or loss) of the circuit
B. Razavi, “RF Microelectronics”, 2nd Ed. 2011

## Slide 19: S-Parameters
B. Razavi, “RF Microelectronics”, 2nd Ed. 2011
S-parameters generally have frequency-dependent complex values
We often express S-parameters in dB

## Slide 20: A Few Definitions
Gain
Insertion loss
Return loss
Agilent Application Note 95-1, “S-Parameter Techniques”
Both insertion loss and return loss should be positive

## Slide 21: Example –HMC-ALH444 Low Noise Amplifier
http://www.hittite.com/products/view.html/view/HMC-ALH444

## Slide 22: Example

## Slide 23: Example
Vendor information;
Measurement Setup.
File Header

## Slide 24: SnP File format
Standard file format for storing and transferring S-parameters
ASCII text
Supports multi-port S-parameters, .snp
Can be imported into EDA software for simulation of the device
SnP (Touchstone) File Format, Agilent Documentation,
http://na.tm.agilent.com/plts/help/WebHelp/FilePrint/SnP_File_Format.htm