## Slide 1: Design of RF & Microwave Systems
Xiaoguang “Leo” Liu
Assistant Professor
School of Electrical and Computer Engineering
Tel: 530-289-6367
lxgliu@ucdavis.edu
http://ucdart.net
EEC 134 A&B
Lecture 5: Building Blocks of RF Systems
– Mixers

## Slide 2: Heterodyne
  “Heterodyning is a radio signal processing technique popularized by Canadian inventor-engineer Reginald Fessenden in 1901, in which new frequencies are created by combining or mixing two frequencies.”
  “The two frequencies are combined in a nonlinear signal-processing device such as a vacuum tube, transistor, or diode, usually called a mixer. In the most common application, two signals at frequencies f1 and f2 are mixed, creating two new signals, one at the sum f1 + f2 of the two frequencies, and the other at the difference f1 − f2. These new frequencies are called heterodynes. Typically only one of the new frequencies is desired, and the other signal is filtered out of the output of the mixer.”
f1
f2
f1 + f2
f1 − f2

## Slide 3: The Ideal Multiplier
A multiplier can realize the mixer function
Consider , and
input
input
output
Sum and difference
frequencies

## Slide 4: Mixer in an RF System
Down-conversion example 1:
  What is the IF frequency?
Down-conversion example 2:
  What is the IF frequency?
Up-conversion example 1:
  What is the RF frequency?
http://www.digikey.com/en/articles/techzone/2011/oct/the-basics-of-mixers

## Slide 5: Image Frequency
Let’s assume ,
  If , what is the IF?
  If , what is the IF?
Signals at the image frequency will be down-converted to IF frequency and corrupted the desired signal
  Even if there is no other signal at the image frequency, noise can still be down-converted, lowering your NF by 3 dB!
  An image reject filter is usually put in front of the mixer to attenuate the signals and noise at the image frequency; more on this later!

## Slide 6: Superheterodyne Receiver
Block diagram with a more modern look
  Principles are still the same
http://mwrf.com/components/quad-demodulators-arm-direct-conversion-receivers

## Slide 7: Mixer Implementations
Fundamentally, mixing (heterodyning) can happen by two mechanisms
  Non-linear circuit
  Linear but time-variant circuit
  (Of course!) non-linear and time-variant circuit

## Slide 8: Mixing by Non-linear Circuit
Example: consider a square-law device (could be a properly biased diode or FET transistor)
+
-
Mixing products
Spurious signals

## Slide 9: Mixing by Non-linear Circuit
Simple diode mixer
  Diodes typically exhibit exponential I-V characteristics, which, at small signals, can be expanded to a polynomial
  Schottky diodes are predominant in mixer applications, particularly at millimeter-wave frequencies, because of their fast transition time
Non-linear region for mixer applications
Mixing

## Slide 10: Diode Mixer
Mixing by non-linear circuit tend to generate a lot of spurious signals
Output frequency spectrum is now more complex than a simple ideal multiplier
BPF
BPF
LPF
We are mostly interested in , the rest of the frequencies are considered as undesired intermodulation products
Isolations between the three ports are provided by filters
  Still, single ended diode mixers are rarely used because of its bad isolation between the ports

## Slide 11: Mixing by Other Forms of Non-linearities
Use transistor non-linearities
Q1
R1
L1
VDC
C1
IF
BPF
BPF
LO
RF

## Slide 12: Mixing by Linear Time Varying Circuit
A simple time-variant circuit consisting of a switch controlled by the LO signal
A square wave can be expanded as
Notes: Add source impedance

## Slide 13: Mixing by Linear Time Varying Circuit
A simple time-variant circuit consisting of a switch controlled by the LO signal
Mixing products
RF Feed-through
Spurs; but not with even order harmonics of the LO

## Slide 14: Mixing by Linear Time Varying Circuit
A balanced LO drive can reduce RF feed-through
Spurs
A=1
A=-1
A=1
A=-1
A balanced (centered at 0) square wave can be expanded as
Mixing products

## Slide 15: Balanced Mixer Designs
Single balanced
  2 diodes for flipping the sign of the RF signal
Double balanced
  A ring of 4 diodes
Double Double-balanced
  Double ring of 8 diodes
http://www.radio-electronics.com/info/circuits/diode_single_balanced_mixer/diode_single_balanced_mixer.php
http://www.minicircuits.com/pages/SIM_Upcon_U712H_int1.htm
http://www.robkalmeijer.nl/techniek/electronica/radiotechniek/hambladen/qst/1993/12/page32/

## Slide 16: Realizing a Switching based Mixer
Diode as a switch
  Use a large (typically 20-dB larger than RF) LO to turn the diode on and off
  Circuit would be identical to a non-linear diode mixer, but much less spurs
LO Drive

## Slide 17: Circuit Implementation of a Multiplier
Gilbert Cell
  A general 4-quadrand multiplier
  Active circuit, so it give gain to the RF signal
  Double balanced
  When used as an RF-mixer, LO signal needs to be large in amplitude so that they can switch the transistors fast
http://www.bessernet.com/articles/mixernoise/mixerNoise6.htm

## Slide 18: Circuit Implementation of a Multiplier
http://www.bessernet.com/articles/mixernoise/mixerNoise6.htm

## Slide 19: Mixer Specifications – Impedance Matching
The need for impedance matching doesn’t need further explanation
However, for switching based mixers, impedance matching can be difficult of the time-varying nature of the circuit
  Impedance matching is really a LTI concept
  Pay attention to the VSWR or return loss specs of mixers!
  Attenuators or isolator/circulators may be needed to improve matching
A=1
A=-1

## Slide 20: Attenuator (Pad) as Matching Network
Attenuators can indeed work as a matching network, and in fact a very wideband one
  Albeit with a lot of signal loss!
300 Ω
10 dB Atten

## Slide 21: Mixer Specifications – Conversion Gain (Loss)
Conversion Gain (Loss): energy conversion efficiency from RF to IF
+
-
Or
  Note that because two mixing products (sum and difference) are generated, there is an automatic 3-dB loss
Active mixers may give gain; while passive mixers (e.g. diode mixers) give loss

## Slide 22: Mixer Specifications – Noise
Single-sideband noise: takes signal from one sideband but noise from both
Double-sideband noise: takes signals and noise from both sidebands
DSB NF would usually be 3-dB less than the SSB NF
For passive mixers, the NF is usually equal to the conversion gain (under the assumption that the mixer is well matched at the RF and IF ports)

## Slide 23: Mixer Specifications – Power Handling
The concept of nonlinearity metrics such as P1dB and IP3 are the same as in amplifiers we studied before
Gain compression – P1dB
Intermodulation – IP3

## Slide 24: Mixer Specifications – Intermodulation
At the IF output, you may have a lot of intermodulation products
Some vendors provide tables of these intermod products (often specified relative to the IF output power)

## Slide 25: Mixer Specifications -- Isolation
Isolation (feed-through): insertion loss between ports (at the same frequency)
  Important ones: LO->RF feed-through, LO->IF feed-through
  Not so important ones:
    RF->IF: typically too small compared with the IF signals
    IF->RF: typically too small compared with the LO->RF feed-through
    IF->LO and RF->LO: typically too small to interfere with the LO circuit
RF
LO
IF
LO-RF feed-through may radiate through the antenna
LO-IF feed-through may interfere with weak IF signals

## Slide 26: Mixer Example: Analog Devices ADL5801
Internal LO amplifier allows a small LO input
All ports are differential

## Slide 27: ADL5801 – Impedance Matching

## Slide 28: ADL5801 – Isolation

## Slide 29: Mixer Example – MiniCircuits MAC-80H+
The level of a mixer is basically the required LO signal level

## Slide 30: Mixer Example – MiniCircuits MAC-80H+