## Slide 1: Design of RF & Microwave Systems
Xiaoguang “Leo” Liu
Assistant Professor
School of Electrical and Computer Engineering
Tel: 530-289-6367
lxgliu@ucdavis.edu
http://ucdart.net
EEC 134 A&B
Lecture 3: Building Blocks of RF Systems
– RF Amplifiers

## Slide 2: Amplifiers in RF/Microwave Systems
The function of an amplifier is simple: to amplify signals
  Recall from last lecture the typical strength of a GPS signal: -125 dBm; that is a ridiculously small power: -125 dBm ≈ 10-15 W!
  We want to make this signal stronger, actually a lot stronger, in order to be able to process it; all without distorting it in any way
  Similar need is in the transmitter: signal generated by the oscillator is often quite weak; needs a lot of amplification before transmitting it in order to reach longer distances
Different kinds of amplifiers are tailored to specific system functions
Power Amplifier
Low Noise Amplifier
Variable Gain Amplifier
Generic Gain Block
Variable Gain Amplifier

## Slide 3: Amplifiers in RF/Microwave Systems
How are RF/microwave transistors made?
  Not much different from low-frequency ac amplifiers; but you need very fast transistors
  A good rule of thumb is to have the transistor’s preferably , where is the transition frequency of the transistor and is the operation frequency of the amplifier.
A common emitter amplifier for RF frequencies
Notes: Include the internal model of the transistor

## Slide 4: Amplifiers in RF/Microwave Systems
How are RF/microwave amplifiers made?
  Not much different from low-frequency ac amplifiers; but you need very fast transistors.
  A good rule of thumb is to have the transistor’s preferably , where is the transition frequency of the transistor and is the operation frequency of the amplifier.
A
input
output
Vcc
GND
Notes: Include the internal model of the transistor

## Slide 5: An Ideal RF/Microwave Amplifier
Infinite bandwidth
Constant gain
Signal travels only from input to output (unilateral)
Perfectly matched at the input and the output
No signal distortion
  Doesn’t add noise to the signal
  Doesn’t change the shape (either in amplitude or phase) of the signal
Amplifies any level of signal
100% efficient
Finite bandwidth
Gain variation, even within the bandwidth
Single feedback from output to input!
Finite (and sometimes intentional ) mismatch at the input/output
Signal distortion
  Noise
  Amplitude
  Phase (less of a concern)
Limited output power (of course!)
<100% efficiency (of course!)

## Slide 6: An Example of a Real-World RF Amplifier
Frequency Range
Gain Variation
Power Limitations
Noise
Linearity (Amplitude Distortion)
Matching
Efficiency

## Slide 7: Amplifier Noise

## Slide 8: Where Does Noise Come From?
Noise sources within typical amplifiers:
  Thermal noise, thermal vibration of bound charges, such as in a resistor
  Shot noise, random fluctuation of charge carriers in an electron tube or solid-state device
  Flicker noise, fluctuation in a direct current, and found in both electron tubes and solid-state devices. Also known as 1/f noise

## Slide 9: Origins of Noise
External:
  Thermal noise from the ground
  Cosmic background radiation from the sky
  Noise from stars (including the Sun)
  Lightening
  Gas discharge lamps
  Radio, TV, and cellular stations (interferers)
  Other wireless devices

## Slide 10: Thermal Noise
A resistor not connected to anything can have a voltage across it
  The average voltage is of course 0 and its amplitude is random and very small
Random motion of charge carriers produce a random variation of voltage (or current) with respect to time  noise voltage and/or noise current
A conductor (equivalently a resistor) has lots of charge carriers
The higher the temperature, the more random motion, and therefore the higher the noise
Higher T
Lower T
Notes: The random motion of the electrons creates a voltage across the two terminals, the

## Slide 11: Thermal Noise – Noise Voltage and Noise Power
The average noise voltage is given by
At low frequencies (f < 5 THz), , therefore
  Noise voltage
  Maximum noise power
h = 6.626 x 10-34 J∙s, Planck’s constant
k = 1.38 x 10-23 J/K, Boltzmann’s constant
B, bandwidth in Hz
f, center frequency of the bandwidth
R, resistance in Ω
T, temperature in Kelvin
* For derivation, refer to: http://www.pas.rochester.edu/~dmw/ast203/Lectures/Lect_20.pdf
*

## Slide 12: Thermal Noise ≈ White Noise
At most RF and microwave frequencies, the thermal noise from a resistor appear uniform with respect to frequency, as is evident from the absence of a frequency variable in the Vn expression
We call this type of frequency independent noise “white noise”

## Slide 13: Noise Temperature
If an arbitrary noise source appears to “white”, it can be approximated by a thermal noise
In other words, the noise source can be approximated by a resistor with a certain equivalent temperature Te, which is determined by how strong the noise source is
N0, noise power in bandwidth B

## Slide 14: (Input Referred) Noise Temperature of an Amplifier
If you have a “noisy” amplifier, it means that there is noise power even when there is no input (no signal or noise)
If we assume the amplifier to be linear, then a noisy amplifier can be model by a noiseless amplifier with an equivalent noise source at the input
Note:
Both input and output are matched
You have to take the amplifier gain G into account

## Slide 15: Noise Factor/Figure
We observe that you get more noise at the output; which means that the signal to noise ratio (SNR) is going to degrade after signal passes through an amplifier
  It is important understand that while amplifiers are great at making your signal stronger, they also make noise stronger!!
We define the degradation of SNR, in linear scale, as the noise factor, often denoted by F
  Noise factor always great then 1!
Noise Factor
More often, you see this ration specified in dB; we call it noise figure (NF)
  NF is more commonly seen in datasheets
  NF is always greater than 0 dB
Noise Figure

## Slide 16: Noise Factor of an Amplifier
In fact, neither noise factor nor noise figure is a very elegant way to specifying the noise of an amplifier because they depend on the input noise level, i.e. they are not intrinsic properties of the amplifier
In addition, noise factor/figure can not describe one port devices
So in order to make sure we can fairly compare different components, noise factor or noise figure are specified under specific conditions
  input is matched to a 50 Ω source resistor
  being held at a specific temperature; by IEEE standard, 290 K

## Slide 17: Noise of a Cascade System
The noise contributions from subsequent stages are suppressed by the preceding stages
It follows that the first stage in a cascade system needs to have low noise and high gain
Amplifiers specifically designed to do this are called low noise amplifiers (LNA)
  LNAs are often designed for the lowest noise, sacrificing efficiency, linearity, and even gain
  To a large extent, LNAs determine the system sensitivity
Important !!

## Slide 18: Derivation

## Slide 19: Noise Figure of a Passive, Lossy Element
Let’s assume that a resistor at the same physical temperature is connected to the input of the network. Since they in thermal equilibrium, the resistor+network can be treated as one noise source at T, the output noise power should be
We can also treat the input resistor as the signal source, then the output noise power should be
A = attenuation, defined as Pin/Pout
B, bandwidth in Hz
T, physical temperature (in Kelvin) of the network

## Slide 20: Noise Figure of a Passive, Lossy Element
Equating the two
Compare with
A = attenuation, defined as Pin/Pout
B, bandwidth in Hz
T, physical temperature (in Kelvin) of the network
Important !!
Notes: Add note on input and output match

## Slide 21: Measurement of Noise Temperature, Figure, Factor
Y-factor method
  The idea is simple: measure the noise from two known noise sources and compare the noise different at the output

## Slide 22: Question: It seems that taking one measurement is enough to calculate Te …
True, but that would be less accurate; you would have to know GB precisely
Taking two measurements allows you to get rid of measurement errors that are common to both measurements
You need two or more measurement points to accurately extrapolate the zero crossing value
Noise power
Input noise temperature
T1
GkTeB
T2

## Slide 23: Question: Would it help if we take more than two measurements?
Yes, but that would require more noise sources
  Good accurate noise sources can be expensive
  Getting two noise sources with drastically different noise temperature can also be difficult
  Remember that temperature is specified in Kelvin; 0°C and 100°C are only about 30% different
Noise power
Input noise temperature
T1
T3
GkTeB
T2
T4

## Slide 24: Linearity, -- or Non-linearity?

## Slide 25: Linearity and Non-linearity
A system is linear if its output can be expressed as a linear combination (superposition) of responses to individual inputs
A
Ideal Amplifier
Non-ideal Amplifier
Notes: Code for drawing the sine:
#Anacondra spyder environment
# -*- coding: utf-8 -*-
"""
Created on Thu Oct 16 11:55:51 2014
@author: Xiaoguang
"""
import numpy as np
#import scipy.constants
from matplotlib.pylab import *
#constants
pi=3.14159265
#variables
n=300 #number of points to plot
w=2*pi
phi=pi*360/30
t=np.linspace(-1.5,1.5,n)
from numpy import sin, cos, exp
y_f=sin(w*t)
y_3f=0.2*sin(3*w*t+phi)
plot(t,y_f)
savefig('tmp1.eps')
plot(t,y_f+y_3f)
savefig('tmp2.eps')

## Slide 26: Linearity
A system is linear if its output can be expressed as a linear combination (superposition) of responses to individual inputs
Linear Region

## Slide 27: Non-linearity
The input/output characteristic of a memory-less nonlinear system can be approximated with a polynomial
linear
nonlinear
RF/microwave Device or Network

## Slide 28: Effects of Non-linearity
Harmonic Distortion
Even-order harmonics result from αj with even j
nth harmonic grows in proportion to Vn
DC
Fundamental
Second
Harmonic
Third
Harmonic

## Slide 29: Harmonic Distortion
More signal loss and distortion
Interference to other systems
Sometimes can be used to create frequency multipliers
GSM900 Band
http://hyperphysics.phy-astr.gsu.edu/hbase/audio/amp.html
Notes: references

## Slide 30
Gain Compression
Gain
Effects of Non-linearity
Fundamental

## Slide 31
Expansive
Compressive
Most RF/microwave component/circuits are compressive
Gain Compression

## Slide 32: Gain Compression
P1dB: power at 1-dB compression
Psat: power at saturation
If you need very good linearity, you should operate a few dBs below the P1dB point; this is called power back-off
Psat

## Slide 33: Gain Compression
Effect on modulated signals
FM signal carries no information in its amplitude and hence tolerates compression
AM contains information in its amplitude, hence distorted by compression

## Slide 34: Gain Compression
Desensitization:
  the receiver gain is reduced by the large excursions produced by the interferer even though the desired signal itself is small.
Notes: The same mathematical derivation also shows that the modulation on the interferer can be transferred to the weak signal of interest. This is called “cross modulation”

## Slide 35: Effects of Non-linearity
Intermodulation
desired
Interferer
A received small desired signal along with two large interferers
Intermodulation product falls onto the desired channel, corrupts signal.

## Slide 36: Intermodulation – the Mathematics
Third-order intermodulation
products (IM3)

## Slide 37: Intermodulation – Two-Tone Test
Two-Tone Test Harmonic Test

## Slide 38: IM3
IM3 products degrades system performance because they are very close to the passband of the system
The power of IM3 products increases with more rapidly than the fundamental output when the input power is increased

## Slide 39: Third-order Intercept Point
Third-order intercept point designates the point where the third-order intermodulation product has the same power as the fundamental output power
  The input power at the IP3 point is call input-referred IP3: IIP3
  The output power at the IP3 point is call output-referred IP3: OIP3

## Slide 40: Third-order Intercept Point
In practice, the amplifier never works close to the IP3 point because it would have saturated way before that
IP3 is extrapolated from measurements of the fundamental output and IM3 products in the linear region of the amplifier
  IP3 is really a measure of linearity, rather than power handling
Notes: In the future, talk about asymmetric IM3 products

## Slide 41: An Example of a Real-World RF Amplifier
Power Limitations
Noise
Linearity (Amplitude Distortion)
Efficiency

## Slide 42: Efficiency

## Slide 43: RF Amplifier Efficiency
Efficiency for an RF device generally gauges how effective it is to generate RF energy from dc energy
  So we could define efficiency as
  Sometimes also called “drain efficiency”
  The rest of the dc energy generally converts to heat, which can be a big problem if the numbers get large
For RF amplifiers, we are actually also sending in RF energy, so we ought to take that part into account
  As an extreme example, let’s say we have an amplifier with . If we send 1 W to the input of the amplifier (assuming that this will not damage the amplifier

## Slide 44: Power Added Efficiency (PAE)
  Takes care of the input power problem
  For high gain (>10 dB), PAE is very close to drain efficiency.
  PAE is the highest at the saturation point and degrades as we back off from saturation
    High linearity requirement will result in low PAE

## Slide 45: Types of RF Amplifiers

## Slide 46: Types of RF Amplifiers
Most vendors categorize RF amplifier by their intended use

## Slide 47: Types of RF Amplifiers
Common types of RF amplifiers
  Low noise amplifiers:
    Optimized for low noise and high gain
  Power amplifiers:
    Optimized for high output power and efficiency
    Gain can be moderate if there is no driver included
  Variable gain amplifiers
    Gain can be changed analogly or digitally
  Linear amplifier
    Optimized for linearity
  Gain block/Driver amplifiers
    General purpose amplifier with well balanced specs
  Wideband amplifiers
    Optimized for wide bandwidth; it’s not uncommon to see decade (10:1) bandwidth amplifiers in this category
Bottom line is: look at the quantitative metrics (noise, linearity, power handling, efficiency, size, cost) when choosing your amplifier

## Slide 48: RF Amplifier Examples

## Slide 49: Low Noise Amplifier (LNA) Examples
Connectorized 2.3 – 2.7-GHz LNA module with 0.8-dB NF (AdaptiveRF, UK)
Waveguide LNA modules up to 100 GHz (NRAO, US)
Packaged LNA IC with 0.27-dB NF (Avago, US)
LNA circuits of a microwave receiver implemented on PCB;
They are easily recognizable as the first block after the antenna feeds (this is a dual-polarization system so there are two feeds)
Notes: https://science.nrao.edu/facilities/cdl/low-noise-amplifiers
http://www.avagotech.com/pages/en/rf_microwave/amplifiers/low_noise_amplifiers/mga-16116/
http://en.wikipedia.org/wiki/Low-noise_block_downconverter

## Slide 50: Low Noise Amplifier (LNA) Examples
A random example: Hittite HMC517LC4
Notes: https://science.nrao.edu/facilities/cdl/low-noise-amplifiers
http://www.avagotech.com/pages/en/rf_microwave/amplifiers/low_noise_amplifiers/mga-16116/
http://en.wikipedia.org/wiki/Low-noise_block_downconverter

## Slide 51: Low Noise Amplifier (LNA) Examples
Notes: https://science.nrao.edu/facilities/cdl/low-noise-amplifiers
http://www.avagotech.com/pages/en/rf_microwave/amplifiers/low_noise_amplifiers/mga-16116/
http://en.wikipedia.org/wiki/Low-noise_block_downconverter

## Slide 52: Low Noise Amplifier (LNA) Examples
Notes: https://science.nrao.edu/facilities/cdl/low-noise-amplifiers
http://www.avagotech.com/pages/en/rf_microwave/amplifiers/low_noise_amplifiers/mga-16116/
http://en.wikipedia.org/wiki/Low-noise_block_downconverter

## Slide 53: Low Noise Amplifier (LNA) Examples
Notes: https://science.nrao.edu/facilities/cdl/low-noise-amplifiers
http://www.avagotech.com/pages/en/rf_microwave/amplifiers/low_noise_amplifiers/mga-16116/
http://en.wikipedia.org/wiki/Low-noise_block_downconverter

## Slide 54: Low Noise Amplifier (LNA) Examples
http://www.digikey.com/product-search/en?FV=fff40036,fff802bc,fffc0467&k=HMC517LC4
Notes: https://science.nrao.edu/facilities/cdl/low-noise-amplifiers
http://www.avagotech.com/pages/en/rf_microwave/amplifiers/low_noise_amplifiers/mga-16116/
http://en.wikipedia.org/wiki/Low-noise_block_downconverter

## Slide 55: Power Amplifier Example
TriQuint TGA2216-SM

## Slide 56: Power Amplifier Example

## Slide 57: Power Amplifier Example
Notice that the pin layout is drawn flipped!

## Slide 58: Power Amplifier Example

## Slide 59: Power Amplifier Example

## Slide 60: Variable Gain Amplifier
Analog Devices ADL5240

## Slide 61: Variable Gain Amplifier
Analog Devices ADL5240

## Slide 62: Variable Gain Amplifier

## Slide 63: Variable Gain Amplifier

## Slide 64: Variable Gain Amplifier

## Slide 65: Variable Gain Amplifier

## Slide 66: Further Reading
“Fundamentals of RF and Microwave Noise Figure Measurements,” Agilent Application Note 57-1.
“Noise Figure Measurements,” Agilent Presentation, 2009
Iulian Rosu, YO3DAC / VA3IUL, “Automatic Gain Control (AGC) in Receivers, “http://www.qsl.net/va3iul/.
“60 dB Wide Dynamic Range, Low Frequency AGC Circuit Using a Single VGA, “ Analog Devices AN-934 Application Note.