## Slide 1: Design of RF & Microwave Systems
Xiaoguang “Leo” Liu
Assistant Professor
School of Electrical and Computer Engineering
Tel: 530-289-6367
lxgliu@ucdavis.edu
http://ucdart.net
EEC 134 A&B
Lecture 4: Building Blocks of RF Systems
– Oscillators and Synthesizers

## Slide 2: RF Oscillator
Oscillator
  RF signal source
  Converts dc energy into RF
Oscillator in an RF system
RF

## Slide 3: Types of Oscillator Design
Multi-vibrator
Ring
Feedback
Negative Resistance

## Slide 4: Multi-vibrator Oscillator
One or more current sources charge and discharge an energy storage element whose voltages flips a comparator (usually with hysteresis) to disconnect or connect the current source(s)
Also called astable or relaxation oscillator
Amplitude is controlled by the thresholds
Start-up is guaranteed (will always oscillate)
Usually used for low frequency (up to a few MHz)

## Slide 5: Feedback Oscillator
While in college, Edwin H. Armstrong observed high frequency oscillation if the output signal of a vacuum tube amplifier is fed back to its input; thus inventing an oscillator which could be used to generate strong signals for radio transmitters
Oscillation can be created by introducing positive feedback
http://en.wikipedia.org/wiki/Armstrong_oscillator
http://en.wikipedia.org/wiki/Regenerative_circuit
Feedback

## Slide 6: Barkhausen Criteria
It states that if is the gain of the amplifying element in the circuit and is the transfer function of the feedback path, so is the loop gain around the feedback loop of the circuit, the circuit will sustain steady-state oscillations only at frequencies for which:
  The loop gain is equal to unity in absolute magnitude, that is, , and
  The phase shift around the loop is zero or an integer multiple of :
In an actual oscillator, the product will initially exceed 1 to start the oscillation; As the oscillation grows, the gain compresses to reach the steady state.

## Slide 7: Realization of the Feedback Oscillator
A frequency selective network is usually used as the feedback network
Most oscillator designs are based on a few classic structures (templates)
Armstrong oscillator
Colpitts Oscillator
Hartley Oscillator
Clapp Oscillator

## Slide 8: Frequency Selective Network
The frequency selective (feedback) network is usually a bandpass network whose center frequency is set the correct frequency
In general, the higher the Q of the frequency selective network, the more stable the oscillation is.
The frequency selective network can be made of a variety of resonator structures
  Simple L-C resonator (Q of 5 ~ 100)
  Transmission line resonator (Q of 30 ~ 250)
  Waveguide/Cavity resonator (Q of 300 ~ 5000)
  Dielectric resonator (Q of 3000 ~ 6000)
  Crystal resonator (Q of 10,000 ~ 200,000!)

## Slide 9: Crystal Oscillators
The “crystal” is a piece of well shaped single crystal piezoelectric material (most commonly quartz) sandwiched between two metal electrodes.
The piezoelectric effect is a property that some materials exhibit: external applied mechanical stress can induce a voltage potential and vice versa.
Quartz is a natural piezoelectric material.
The piezoelectric effect serves as a transduction mechanism, converting electric signals into mechanical vibration and back to electric signal again
The transduction is the strongest when the crystal oscillates at its natural frequency which is determined by the shape of the crystal

## Slide 10: Crystal Oscillators (cont.)
Because of the extremely high Q, crystal oscillators are often used as very stable frequency sources.
The frequency of crystal oscillators are in the range of ~10 kHz to ~100 MHz.
  The frequency is primarily determined by the size and shape of the crystal. The lower frequency is usually bound by the crystal size; the higher end bound by the precision of machining the crystal.
The frequency of a crystal oscillator (XO) is temperature dependent, which is an undesirable effect.
  Temperature compensated crystal oscillator (TCXO) are designed carefully to reduce the temperature dependence
  Oven controlled crystal oscillator (OCXO) uses active temperature control to maintain a stable temperature around the crystal for the best stability. Downside is that it burns power and needs start-up (warm-up) time.

## Slide 11: Another Oscillator Design Perspective
Let’s look at oscillation of voltage/current in a resonant circuit
The quality factor (Q) determines the damping (loss) of the system
  The higher the Q, the lower the damping, the longer the oscillation lasts
  In all practical systems, the oscillation eventually dies down

## Slide 12: Sustaining the Oscillation – Negative Resistance
If we can replenish the dissipated energy in a resonator, we could possibly sustain the oscillation
Adding a “negative resistance” device will do the trick
  A positive resistance dissipates energy; a negative resistance generates energy

## Slide 13: Creating Negative Resistance
How do we realize negative resistance?
  I-V curves with negative slope
  Positive feedback provides effective negative resistance; the idea of a negative resistance oscillator is unified with a feedback oscillator

## Slide 14: Creating Negative Resistance
How do we create negative resistance?
  Some semiconductor devices exhibit negative resistance naturally; the mechanism cannot be described clearly with positive feedback
  The microwave Gunn diode is a great example
  Can be placed into a high-Q cavity resonator to generate oscillation
http://www.eevblog.com/forum/projects/gunn-oscillator-doppler-radar-transceiver/
http://en.wikipedia.org/wiki/Gunn_diode
Negative I-V curve

## Slide 15: Ring Oscillator
Frequency is determined by the delay of amplifiers (inverters)
Guaranteed start up.

## Slide 16: Oscillator Specifications
Output power
  Some oscillators have built in buffer/driver amplifiers to improve the output power, obviously at the penalty of high dc power consumption
Harmonics
  In reality, the voltage/current waveform in an oscillator is not purely sinusoidal. Some distortion is usually present, resulting in harmonic content in the output spectrum.
http://spectrum.ieee.org/consumer-electronics/audiovideo/the-cool-sound-of-tubes/3/distortion

## Slide 17: Oscillator Specifications – Pushing
In practical oscillators, the active circuit characteristics will be influenced by the supply voltage
  e.g. recall that a transistor’s IV characteristics are functions of both gate (base) and drain (collector) voltages
  Fluctuation in the supply voltages can result in fluctuation in the oscillator output frequency and power
Oscillator frequency pulling is specified as the frequency shift per volt change in the supply voltage: Hz/V, or Hz/mV, kHz/mV, MHz/V, or any other variants
To counteract pushing, some oscillators integrate a voltage regulator/reference
http://www.ittc.ku.edu/~jstiles/622/handouts/Pushing%20and%20Pulling.pdf
Shunt
voltage reference

## Slide 18: Oscillator Specifications – Pulling
The load impedance of an oscillator can also affect the oscillator output performance
  e.g. consider a conceptual Collpitts oscillator shown in the left: the capacitance in the load becomes part of the frequency selective network, which may shift the resonant frequency and the output power of the oscillator. The pulling characteristics in a real oscillator may be much more complex.
  Because impedance is a complex number, there is not a single quantity to quantify pulling, a typical specification could read “less than 2 MHz at VSWR = 3”; this is usually the worst-case specification.
To counteract pulling of an oscillator, the output is usually isolated from the load by an isolator/circulator, amplifier, or simply an attenuator.

## Slide 19: Oscillator Characteristics – Locking
When oscillators are coupled with each other, they tend to synchronize in phase and frequency
  Watch a video on mechanical oscillators synchronizing in phase
  Same phenomena can be observed in electronic oscillators – we call it injection locking or pulling (when the initial frequency or phase difference is too great to achieve total synchronization)
Locking can be used to our advantage
  E.g. clock distribution – locking many oscillators to the same frequency reference
Unwanted locking can also be detrimental to an RF system
http://ieeexplore.ieee.org/xpls/abs_all.jsp?arnumber=1327738&tag=1
Undesirable Effects of Injection Pulling
Synchronization of mechanical oscillators

## Slide 20: Phase Noise
Phase noise is a very important system parameter and is worth learning a little more about
Phase noise results from
  imperfect frequency selectivity of the feedback network
  noise sources that modulates the high frequency current/voltage that passes through the active (gain) part of an oscillator
  Noise (mostly thermal) from loss components in the passive part of the circuit
Phase noise is usually specified with respect to the carrier power: dBc, in which “c” means carrier. Also, because phase noise shows itself as a continuous spectrum, its power is measured within a certain bandwidth, hence the unit of “dBc/Hz”
http://www.mti.com.tw/_english/06_center/02center.php?MainID=9&ID=57
http://www.digikey.com/en/articles/techzone/2010/dec/converting-oscillator-phase-noise-to-time-jitter

## Slide 21: Phase Noise – Leeson’s Formula

## Slide 22: Voltage Controlled Oscillator (VCO)
An oscillator whose output frequency can be controlled by a voltage signal
Usually implemented by tuning the feedback network by a variable capacitor
Very useful component in any system whose operating frequency needs to change
  FM radio
  Frequency sweeping radars
  Frequency synthesizers
  Spectrum analyzers
  Network analyzers
RF
Vtune

## Slide 23: VCO Specifications
All the specifications for fixed oscillators are still applicable
Tuning sensitivity: frequency change per volt of tuning voltage change
  Sometimes referred to as “VCO gain”
  Specified in Hz/V, or MHz/V
  A higher sensitivity means that you can cover a large frequency range with small tuning voltage; it also means that the output frequency is more sensitive to the noise in the tuning voltage
In some applications, particularly frequency modulation (FM) systems, tuning linearity is of particular concern
  Good linearity ensures good modulation fidelity
Mini-Circuits

## Slide 24: Example VCO Datasheet
Mini-Circuits ZX95-1300+

## Slide 25: Example VCO Datasheet (cont.)

## Slide 26: Example VCO Datasheet (cont.)

## Slide 27: Example VCO Datasheet (cont.)

## Slide 28: Phase-Locked-Loop (PLL)
A feedback loop to achieve very high frequency stability and low phase noise
Also a very useful technique to accurately track the frequency and phase of the input signal
Read more: http://www.analog.com/library/analogDialogue/archives/33-03/phase/index.html
Crystal frequency
reference

## Slide 29: Phase Detector
Transfer function
XOR as a simple implementation
KPD
http://www.seas.ucla.edu/brweb/teaching/215C_W2013/PLLs.pdf

## Slide 30: Modeling the VCO
Assuming that the VCO has a linear tuning characteristics and its sensitivity/gain is KVCO
A higher frequency means faster phase progression
http://www.seas.ucla.edu/brweb/teaching/215C_W2013/PLLs.pdf

## Slide 31: Phase/Frequency Detector and Charge Pump
The phase detector (PD) detects the phase difference between the two incoming signals and outputs a voltage/current that is proportional to this difference
A phase frequency detector (PFD) maintains correct output even when the input signal frequency is different

## Slide 32: Example
The PFD allows the use of charge-pump circuits to create the control signal for the VCO
http://www.seas.ucla.edu/brweb/teaching/215C_W2013/PLLs.pdf
Low-pass filter smooths out the pulses
VCO
Increase in Vcont (VTUNE) bumps up the frequency and therefore the phase progression so that the VCO output phase can catch up with the Vin (Vref) phase

## Slide 33: Phase/Frequency Detector
The phase/frequency detector (PFD) provides the correct output even when the frequencies of the two inputs are different
http://www.seas.ucla.edu/brweb/teaching/215C_W2013/PLLs.pdf

## Slide 34: PFD+ Charge Pump (CP) in PLL
The charge pump provides the current to drive the subsequent stage in the PLL
The PLL locks the output signals phase and frequency to the reference: we can now replicate the stability and low phase noise of the reference!
PFD
CP
LPF
http://www.seas.ucla.edu/brweb/teaching/215C_W2013/PLLs.pdf

## Slide 35: Phase Noise in a PLL
A PLL is basically a negative feedback look that stabilizes the output signal to the reference.
The stabilization only takes effect within the loop bandwidth—effectively the bandwidth of the low-pass filter.
http://www.analog.com/library/analogDialogue/archives/33-05/phase_locked/index.html
http://electronicdesign.com/analog/adc-performance-what-s-jitter-got-do-it

## Slide 36: Frequency Synthesis – Integer-N Synthesizer
The basic PLL studied above isn’t very useful for frequency synthesis; the output signal frequency is the same as the reference!
Adding a divide by N block:
  Output frequency now a multiple of the reference frequency
  By digitally controlling the divider ratio N we can generate different frequencies
  Drawback: Output frequency resolution is determined by the reference frequency
  One penalty paid is the phase noise: Phase noise grows 6 dB per multiple by 2, or 20 dB per multiple by 10, in frequency
http://www.seas.ucla.edu/brweb/teaching/215C_W2013/Synthesizers13.pdf

## Slide 37: Integer-N Synthesizer – Adding a Reference Counter
A reference counter can improve frequency resolution
Drawback: the reference counter R makes the feedback counter very large!
Example:
  Using a 10 MHz reference clock and a reference counter of 1,000, we can achieve frequency resolution of 10 kHz
  To get an output frequency around 900 MHz, we’d need a N value of 90,000 -> equivalent of a 17-bit counter, difficult to make it working right at high frequency
Mark Curtin and Paul O’Brien, “Phase-Locked Loops for High-Frequency Receivers and Transmitters,” Analog Dialogue 33-3, 1999

## Slide 38: Integer-N Synthesizer – Prescalar
Adding a pre-scalar to alleviate the issue: the division is now done in two steps
  The pre-scalar is a high-frequency component that divide the feedback signal by a fixed ratio, e.g. /2, /4, /8, /32, etc
  Because P is fixed, the frequency resolution degrades by P ! Now we seem be going in circles!
    Fortunately P is usually much smaller than R, so we still get a net gain
    And another clever solution exists to solve this issue
Mark Curtin and Paul O’Brien, “Phase-Locked Loops for High-Frequency Receivers and Transmitters,” Analog Dialogue 33-3, 1999

## Slide 39: Integer-N Synthesizer – Dual Modulus Prescalar
Counter A and counter B time-outs sequentially to toggle the prescalar value by 1
  Both A and B can be digitally controlled
Mark Curtin and Paul O’Brien, “Phase-Locked Loops for High-Frequency Receivers and Transmitters,” Analog Dialogue 33-3, 1999

## Slide 40: Fractional-N Synthesizer
Fractional-N synthesizer shifts the modulus of the divider randomly to achieve lower phase noise
It also achieves greater frequency resolution and faster switching time
And it’s too complicated for this class, so we won’t discuss it further.
Mark Curtin and Paul O’Brien, “Phase-Locked Loops for High-Frequency Receivers and Transmitters,” Analog Dialogue 33-3, 1999